## Slide 1: Self-driving vehicle
Lessons learned from a Real-time image recognition project
Gene Olafsen

## Slide 2: Hardware
Modified SunFounder Rasperry Pi video car kit

## Slide 3: Single-board ARM-based computer
RaspberryPi 3
SoC: Broadcom BCM2837
CPU: 4× ARM Cortex-A53, 1.2GHz
GPU: Broadcom VideoCore IV
RAM: 1GB LPDDR2 (900 MHz)
Networking: 10/100 Ethernet, 2.4GHz 802.11n wireless
Bluetooth: Bluetooth 4.1 Classic, Bluetooth Low Energy
Storage: microSD
GPIO: 40-pin header, populated
Ports: HDMI, 3.5mm analogue audio-video jack, 4× USB 2.0, Ethernet, Camera Serial Interface (CSI), Display Serial Interface (DSI)

## Slide 4: software
Python
TensorFlow
Keras
OpenCV

## Slide 5: Develop a Model
Follow a line...

## Slide 6: Drive with XBOX Controller
https://github.com/FRC4564/Xbox

## Slide 7: Define a path
Rope or Tape

## Slide 8: Data Collection
Images and Steering Angle
433

## Slide 9: Pulse width modulation and servo

## Slide 10: Image augmentation
https://github.com/aleju/imgaug

## Slide 11: Code
sometime = lambda aug: iaa.Sometimes(0.3, aug)
sequence = iaa.Sequential([
# blur images with a sigma between 0 and 3.0
sometime(iaa.GaussianBlur((0, 1.5))),
# sharpen images
sometime(iaa.Sharpen(alpha=(0, 1.0), lightness=(0.75, 1.5))),
# add gaussian noise to images
sometime(iaa.AdditiveGaussianNoise(loc=0, scale=(0.0, 3.), per_channel=0.5)),
# randomly remove up to 10% of the pixels
sometime(iaa.Dropout((0.0, 0.1))),
# dropout variant
sometime(iaa.CoarseDropout((0.10, 0.30), size_percent=(0.02, 0.05), per_channel=0.2)),
# change brightness of images (by -10 to 10 of original value)
sometime(iaa.Add((-10, 10), per_channel=0.5)),
],
random_order=True # do all of the above in random order
)

## Slide 12: Model
Layer (type) Output Shape Param #
=================================================================
input_1 (InputLayer) (None, 80, 160, 3) 0
_________________________________________________________________
conv2d_1 (Conv2D) (None, 78, 156, 16) 736
_________________________________________________________________
conv2d_2 (Conv2D) (None, 76, 152, 16) 3856
_________________________________________________________________
max_pooling2d_1 (MaxPooling2 (None, 19, 76, 16) 0
_________________________________________________________________
conv2d_3 (Conv2D) (None, 17, 72, 32) 7712
_________________________________________________________________
conv2d_4 (Conv2D) (None, 15, 68, 32) 15392
_________________________________________________________________
max_pooling2d_2 (MaxPooling2 (None, 3, 34, 32) 0
_________________________________________________________________
conv2d_5 (Conv2D) (None, 3, 34, 4) 132
_________________________________________________________________
flatten_1 (Flatten) (None, 408) 0
_________________________________________________________________
dense_1 (Dense) (None, 1) 409
=================================================================
Total params: 28,237
Trainable params: 28,237
Non-trainable params: 0

## Slide 13: network
# Construct the network# Const
image_inp = Input(shape=(FRAME_H, FRAME_W, 3))
x = Conv2D(filters=16, kernel_size=(3, 5), activation='relu', padding='valid')(image_inp)
x = Conv2D(filters=16, kernel_size=(3, 5), activation='relu', padding='valid')(x)
x = MaxPooling2D((4, 2))(x)
x = Conv2D(filters=32, kernel_size=(3, 5), activation='relu', padding='valid')(x)
x = Conv2D(filters=32, kernel_size=(3, 5), activation='relu', padding='valid')(x)
x = MaxPooling2D((4, 2))(x)
x = Conv2D(filters=4, kernel_size=(1, 1), activation='linear', padding='same')(x)
x = Flatten()(x)
x = Dense(1, activation='tanh', kernel_regularizer='l1')(x)
angle_out = x
model = Model(inputs=[image_inp], outputs=[angle_out])

## Slide 14: collaborate
Collect the image and steering training data during MW-MLG meetings!
Train the model.
Deploy the trained model and see how well it performs.
Make the training data public (GitHub).
Modify the model, train and deploy during future meetings.

## Slide 15: Future Enhancements
Modulate speed approaching a curve
Observe 'traffic' signs
Avoid obstacles

## Slide 16: Toolchain
MobaXterm – SSH Terminal and X-Windows Server
  https://mobaxterm.mobatek.net/
Linnode – hosting
  https://www.linode.com/
CodeAnywhere – Browser-based SSH, Text Editor
  https://codeanywhere.com/
Git – Source/Data Repository
  https://github.com/

## Slide 17: Issues and lessons learned
While this project is inspired by self-driving model car projects that already exist, there is nothing for the vehicle platform or controller which was selected.

## Slide 18: Image capture
Initial attemps to capture training data failed miserably because images produced were too dark.
To correct the issue, a number of very bright LED 'headlights' were added to the vehicle.

## Slide 19: POWERing the platform
Developing the capture software and ultimately the program which will load the model and predict the steering angle must be debugged on the actual test vehicle.
For the time where engaging the motors is not necessary, the Raspberry Pi can be powered from another computer's USB port.
Testing the data capture with the steering and drive motors functioning reduces battery life to about 20 minutes.
Even with multiple batteries, it was difficult to work in a 20 minute window.

## Slide 20: Power distribution
7.4V
DC-DC Converter
5V
Raspberry Pi
Servo Controller
DC Motor Driver
Dual 18650 Li-Ion Cells
AC Power Adapter

## Slide 21: DC Motor Driver
The driver is built based on 11 L298N. As a high-voltage and large-current chip for motor driving, encapsulated with 15 pins, the chip has a maximum operating voltage of 46V and an instant peak current of as high as 3A, with an operating current of 2A and rated power of 25W. Thus, it is completely capable of driving two low-power DC motors.

## Slide 22: Step-down dc-dc converter
Based on the chip XL1509, the module converts the battery output of 7.4V to 5V, so as 10 to supply power to Raspberry Pi and the servo. As a DC to DC converter IC, the chip has an input voltage ranging from 4.5V to 40V and generates an output voltage of 5V with a current of as high as 2A.

## Slide 23: Initial training attempts
I decided originally to provide a long continuous line on which to train the vehicle.
The gamepad controller is used to steer the vehicle as it collects images and steering angle information.

## Slide 24: Testing the model
Upon collecting the data, training the model and observing instance execution- the steering response to visual input was ineffective. In fact, there was almost no steering response produced- no matter what input was provided to the camera. The steering servo simple shuttered with a seemingly random response to any input.

## Slide 25: Training Data Analysis
Upon collecting the data, training the model and observing instance execution- the steering response to visual input was ineffective.
The data consisted of mostly 'straight' steering angle values.
Most of the driving is done in straight lines, with little continuous steering adjustment.

## Slide 26: Practice driving circles
To capture many training instances with a 'large' steering angle, I decided to train the vehicle on circles of different radii.
The plan is to be able to apply roughly a continuous input to the variable steering for each of the different radii.

## Slide 27: DATA cAPTURE

## Slide 28: Camera position
The camera was repositioned to 'look' lower toward the ground in front of the vehicle. This change was mde so that the car could respond to sharper turns.

## Slide 29: POWERED capture
Capturing a large number of training instances requires running the vehicle for extended periods of time... that means, no batteries.
For each circle- the vehicle is 'driven' clockwise for 2 or 3 revolutions and then counter-clockwise for 2 or 3 revolutions. This procedure captures labeled training data. Finally, the same circle is driven again 2 or 3 revolutions both clockwise and counterclockwise AGAIN to capture labeled validation data.
The radius of the circle is increased a set amount. (about 2-3 inches)

## Slide 30: Powered capture Rig

## Slide 31: Capture, training, deploy steps
The data is captured to the RaspberryPi's SD card.
The training and validation data is uploaded to Github.
The Linode machine clones the data repository.
The model is trained and the weights.hdf5 file is uploaded to Github.
The weight file is retrieved from Github on the RaspberryPi.